## Slide 1: WSN@home and IoT Peter Van Aken

## Slide 2: What can you expect from this session ?
How to build a low energy, low cost WSN yourself,
How WSN can be applied in YOUR home,
Demo of live WSN@home
…path forward …
Let’s start with a couple of facts …

## Slide 3: Facts … temperature
Meet Anna…smart, beautiful and cool …

## Slide 4: Facts … weather

## Slide 5: Facts … light

## Slide 6: Facts …smart cars, watch…etc

## Slide 7: What does IoT means for me?
It is reality … being built today
All different type of things connected to the internet …
But basically it is about:
    data,
    networking,
    measuring (via sensors) and controlling (through actuators)
…it is/will changing/change the way we’re living

## Slide 8: Home automation protocols
X10 :
  1975 / domotica
  Power line & RF (433Mhz)
  60 bps
  Used EU : +
UPB : (Universal powerline bus)
  1999 / Powerline only
  120 bps
  Used EU : --

## Slide 9: Home automation protocols
Insteon
  2005
  Power line & RF (916Mhz)
  Meshing topology
  180 bps
  Used EU : - / ++ (USA)

## Slide 10: Home automation protocols
Z-wave
  2008
  RF (868/916Mhz)
  Meshing topology
  100 kbps
  Used EU : +
  E.g http://www.fibaro.com/en

## Slide 11: Home automation protocols
Zigbee
BLE
Velbus
KNX
CAN
Wifi
EnOcean
…and growing

## Slide 12: Home automation protocols
Conclusion :
  huge amount of protocols,
  wired & wireless,
  Licensed and license-free,
  high power / low power / no power
  …so, why not adding an own protocol to the list and start from my requirements looking at home …

## Slide 13: My requirements
Wireless :
  easy to install in existing house
Mixed power
  Powerplug and battery
Low cost
Secure
Sensors / actuators
  Tranceiver
Meshing network
  low power
Accessible from anywhere and any device

## Slide 14: WSN@home in action
DEMO

## Slide 15: Different component in WSN ?
Sensor/actuator Node : measure/control
Gateway : connect nodes <-> controller
Controller : connect network to UE/Internet

## Slide 16: WSN@home breakdown
Nodes :
  Common platform :
    uC : Atmel atmega328P (8bit AVR / 32KB flash / 1.8v-5.5v operation)
    RF : nordic NRF24L01+ (ultra LP (nA) / 2Mbps / ISM band / transceiver / 1.9v-3.6v operation)
    Both can be powered from 3v supply = 2xAA/2xAAA/CR2032…
  Specific standard interface : i2C (TWI), SPI, onewire, serial
  Lots of prototyping platforms available for uC : Arduino UNO, nano, pro mini, …

## Slide 17: WSN@home breakdown
Nodes :
  Different RF modules : onboard/external antenna, PA (power amplifier), LNA (Low Noise amplifier), SMD/die/TSOP : open air range : 30 – 1100 m
  Firmware :
    baremetal, specific bootloader for OTA
    “mySensors” stack (http://www.mysensors.org)
    Interface specific
    +-30% mem utilisation

## Slide 18: WSN@home breakdown
Nodes :
  Cost

## Slide 19: Node examples
Temperature node :
  Specific interface :
  onewire
  Sensor : DS18B20
  cost
Electricity node :
  Specific interface : RS485/Modbus
  Sensor :
  cost

## Slide 20: Node examples
Water/gas node
  Specific interface : digital input
  Sensor : Hall effect switch a3121eua
  Cost

## Slide 21: Node examples
Solar boiler node
  Specific interface : RS232
  Sensor : ROTEX Solaris RPS3
  Cost /

## Slide 22: Gateway : commercial
Ethernet

## Slide 23: WSN@home breakdown
Gateway :
  Common platform same as node : uC + RF
  802.3 (10/100 Mbps) / wiznet W5x00
  RTC / display / reset button
  Firmware :
    baremetal, no bootloader
    NRF24l01+ : mySensors stack (http://www.mysensors.org)
    Reduced MQTT (http://mqtt.org/) client (IP stack / wiznet W5100)
    +-99% mem utilisation

## Slide 24: WSN@home breakdown
Gateway :
  cost

## Slide 25: MQTT
MQ (message queueing) telemetry transport (http://mqtt.org/)
Lightweight protocol on top of TCP/IP (e.g. facebook messenger)

## Slide 26: WSN@home breakdown
Gateway :
  3D printed case, designed in OpenSCAD (http://www.openscad.org/)

## Slide 27: WSN@home breakdown
Controller :
  Openhab (http://www.openhab.org/)

## Slide 28: WSN@home breakdown
Controller :
…but the real power are the BINDINGS (https://github.com/openhab/openhab/wiki/Bindings)
…including MQTT

## Slide 29: WSN@home breakdown
MQTT
LAN
Controller

## Slide 30: About RF
ISM (Industrial, Scientific and Medical) band : license free
Short range band (433/868/916MHz)

## Slide 31: About RF : interference
Whatever you use, think about interference : (remote, alarm, microwave (=2.45GHz), Wifi, Bluetooth,…)
http://www.nordicsemi.com/eng/Products/2.4GHz-RF/nRF24L01
2.476Ghz

## Slide 32: About RF : path losses
Friis transmission equation
Receive power increase by :
  Higher TX power
  Better antennas
  Shorter distance
  Lower frequency
* Power * ANTENNE
* Control distance
(MESHING)

## Slide 33: Todo…
Nodes :
  Design :
    OTA
    encryption,
    Proto PCB -> fab
  Proto :
    mailbox, doorbell,
    smart CV,PIR,
    garage, light, …
Debug/test : Wifi sniffer
Gateway : multi-RF / ESP8266
Controller : rules, rules, rules…

## Slide 34: Interested in …
Which sensor node do you want to build ?
WSN@work ?